ESP32-SBC-FabGL
User Manual
Rev.2.0	April 2024	olimex.com
# Introduction to ESP32-SBC-FabGL

ESP32-SBC-FabGL is Open Source Hardware board designed to work with FabGL library.
It has these features:
- ESP32-WROVER-E module
- VGA connector
- PS2 keyboard connector
- PS2 mouse connector
- Buzzer
- Audio 3.5mm connector
- AccessBus connector for Serial port master processor
- LCD connector (FabGL support LCD or VGA output)
- CH32V003 co-processor for UEXT port handling
- USB-C power and programming/debug connector
- SY8089A 3.3V 2A (3A peak) DCDC power supply
- Lipo charger and battery connector
- UEXT connector (pUEXT 1.0 mm step connector)
- Dimensions: (104 x 68)mm

## Order codes for ESP32-SBC-FabGL and accessories

ESP32-SBC-FabGL	FabGL board with VGA keyboard mouse
BOX-ESP32-FabGL	Custom plastic box
CABLE-USB-A-C-1M	USB-C cable 1 meter
BATTERY-LIPO1400mAh	Lipo battery 3.7V 1400mAh
UEXT modules	There are temperature, humidity, pressure, magnetic field, light sensors.	Modules with LCDs, LED matrix, Relays, Bluetooth, Zigbee, WiFi,	GSM, GPS, RFID, RTC, EKG, sensors and etc.

# HARDWARE

## ESP32-SBC-FabGL layout

## ESP32-SBC-FabGL schematic sources

ESP32-SBC-FabGL latest schematic is on GitHub

## UEXT connector:

UEXT connector stands for Universal EXTension connector and contain +3.3V, GND, I2C, SPI, UART signals. UEXT connector can be in different shapes and sizes but the original UEXT connector is 0.1” 2.54mm step boxed plastic connector. All signals are at 3.3V levels.

As the boards become smaller and smaller some smaller packages were introduced too beside the original UEXT connector
- mUEXT is 1.27 mm step boxed header connector which is with same layout as UEXT
- pUEXT is 1.0 mm single row connector (this is the connector used in RP2040-PICO30)

Olimex has developed number of MODULES with this connector. There are temperature, humidity, pressure, magnetic field, light sensors. Modules with LCDs, LED matrix, Relays, Bluetooth, Zigbee, WiFi, GSM, GPS, RFID, RTC, EKG, sensors and etc.

## AccessBus connector:

Pin1. is marked with a square pad, all others are round pads.
# LCD hat connector:
Pin1. is marked with a square pad, all others are round pads.
# SOFTWARE

ESP32-SBC-FabGL is tested and works with many projects, start with the Olimex fork of FabGL project: https://github.com/OLIMEX/FabGL

Also make sure to check these FabGL articles at our wordpress:

https://olimex.wordpress.com/2023/06/27/esp32-sbc-fabgl-update-now-you-can-play-invaders-with-wii-nunchuck-via-the-uext-port/

https://olimex.wordpress.com/2023/08/01/esp32-sbc-fabgl-how-to-work-with-the-expander-module-gpios-from-fabgl-library-and-apps/

https://olimex.wordpress.com/2023/05/31/zx-espectrum-emulator-tested-with-esp32-sbc-fabgl-the-mensch-computer-with-w65c256-got-vga-display-and-keyboard/

https://olimex.wordpress.com/2023/05/25/new-open-source-hardware-design-is-verified-esp32-sbc-fabgl-single-board-computer-based-on-fabgl-library-with-ps2-keyboard-mouse-and-vga-display-with-many-retro-computer-emulators/

Other projects that we haven’t tested fully but should work:

https://github.com/uho/ESP32forthStation
https://github.com/OulanB/OricVGA32
https://github.com/guidol70/RunCPM_VGA32
https://github.com/EremusOne/ZX-ESPectrum-IDF
https://github.com/rpsubc8/ESP32TinyMCUMEesp81
https://github.com/rpsubc8/ESP32TinyNesMaster
https://github.com/rpsubc8/ESP32TinyZXSpectrum
https://github.com/rpsubc8/ESP32TinyFairChild
https://github.com/rpsubc8/ESP32TinyChip8
https://github.com/rpsubc8/ESP32TinyFake86
https://github.com/rpsubc8/ESP32TinyCPC
https://github.com/rpsubc8/ESP32TinyC64

# Document revision History
Revision 1.0 May 2023
Revision 2.0 April 2024